## Slide 1: Developing Robust Autonomous Wall-Following Algorithms
Team 13 Lab 3 Briefing
Xavier (2A), Insuh (16), Inimai (6-2), Russell (6-2)
3/10/25

## Slide 2: Our Goal
Develop a robust method for autonomous wall-following
Navigate new environments
Use LIDAR
Avoid collisions
Follow some desired path

## Slide 3: Technical objectives
Effective safety controller: brakes to interrupt collision trajectories, but does not stop prematurely when merely driving close to the wall
Effective wall-following algorithm: maintains a desired wall distance with minimal oscillation, and quickly converges to this behavior in response to disturbances (turns, stop/start)

## Slide 4: From Simulation to Racecar
Well-defined walls / obstacles
Ideal physics (0 stop distance)
Low noise signal
Collisions are ok when testing
Imperfect hardware response to commands
Prevent collisions (safety controller)
Possibly mid-noise signal

## Slide 5: Technical Overview
Wall follower is built around PID control
Safety controller works on principle of stopping distance

## Slide 6
Steering output as a linear, weighted sum of distinct error quantifications
Defining our PID approximation
approx derivative
discretized integral

## Slide 7: Wall follower iteration in sim
LiDAR measurements
Filtered data (general)
Filter by angle & distance
Linear Regression
Estimate wall line & car position
Robot Actuator
Robot distance from the wall
Ackermann CMD
Side
Wall Follower (PID)
wall side
desired distance
velocity
front-distance
previous error
Technical Overview
Filtered data (front-facing)
Notes: Weight error by mean front-facing [-pi/6, pi/6] LIDAR distance
Forces tight turns when coming up against a wall

## Slide 8: Wall follower iteration in sim
LiDAR measurements
Filtered data (general)
Filter by angle & distance
Linear Regression
Estimate wall line & car position
Robot Actuator
Robot distance from the wall
Ackermann CMD
Side
Wall Follower (PID)
wall side
desired distance
velocity
front-distance
previous error
+ cumulative error
Technical Overview
Filtered data (front-facing)
Notes: Weight error by mean front-facing [-pi/6, pi/6] LIDAR distance
Forces tight turns when coming up against a wall

## Slide 9: Safety controller to prevent crashes.
π/3
Buffer distance
Technical Overview

## Slide 10: Safety controller to prevent crashes.
π/3
Buffer distance
DOES NOT scale well with changing velocities
Technical Overview

## Slide 11: Stopping distance is proportional to car velocity squared.
Velocity (m/s) Car is Driving At | Stopping Distance (m)
0.25 | .06
0.5 | .08
0.75 | .10
1 | .11
1.25 | .24
1.5 | .43
1.75 | .41
2 | .47
2.25 | .558
Technical Overview

## Slide 12: To prevent crashes, we implemented a safety controller.
π/3
Buffer distance
Distance to bumper
Stopping distance
Extra buffer
Technical Overview

## Slide 13: To prevent crashes, we implemented a safety controller.
Distance to bumper
Stopping distance
Extra buffer
Too safe for obstacles at angles far from 90 degrees
Can handle changing velocities
Technical Overview

## Slide 14: To prevent crashes, we implemented a safety controller.
Distance to bumper
Stopping distance
Extra buffer
ADD for steering angle commands not at 90 deg:
Distance to bumper
Stopping distance
Extra buffer
Technical Overview

## Slide 15: Our Evaluation
what is an effective wall-follower?
Robust to disturbances (turns, start/stop)
Converges quickly to desired path
Differentiate collision cases from safe navigation

## Slide 16: Safety Controller
!
Steady operation near wall
Curved path < safe distance
1) Slow
2) Stop
3) Re-steer
Evaluation
Notes: When driving close to wall, safety should not kick in, but if the steering turns towards the wall and the trajectory to wall is too close, racecar should stop, leave a buffer zone, and change steering to minimize damage in the event of a collision.
Reasoning, testing:
This is important to the functionality of the safety controller. The controller should only take over navigation to prevent an impending collision, but ideally it will be able to differentiate between uncontrolled proximity and controlled proximity as created by an effective wall following algorithm.
Given a working wall-follower, we can test the effectiveness of the controller by:
decreasing the desired wall distance until the combined safety, wall follower stops the car
disabling the safety controller
Testing to see if the wall follower is able to successfully control the car at that distance
  If not, the safety controller did its job
  If it can, the safety controller is too protective
Note, the safety controller should also not allow the car to crash at any point -> this indicates under-protection

## Slide 17: Wall Follower
(Target Distance)
(Acceptable Error Amplitude)
]
(Convergence Time)
= ∫error
Evaluation
Notes: Wall follower:
Track number of oscillations, or elapsed time, until error amplitude converges below some threshold
Track averaged error over time between proximity and desired distance

## Slide 18: Results
Visualize:
Safety controller: test to failure
Wall follower: averaged error, oscillations until error converges

## Slide 19: Conclusions
1) our wall follower uses PID control to maintain desired distance to wall
Tested with oscillatory convergence, average error

## Slide 20: Conclusions
1) our wall follower uses PID control to maintain desired distance to wall
Tested with oscillatory convergence, average error
2) our safety controller builds a buffer zone around the car based on velocity
Tested by finding limit case